## Slide 1: Energy Aware Modeling Demo
Accellera SLDS-Rosetta Committee
Information and Telecommunication Technology Center, University of Kansas
The Adelaide Rosetta Project (TARP), Adelaide University

## Slide 2: Demonstration
Demonstration Goals
  Address a prototypical embedded system or subsystem
  Write specifications of functional and constraint models
  Demonstration interaction between models from different semantics
  Demonstrate prototypical analysis activities
Selected Target System
  TDMA communications subsystem common in embedded systems
  Model functional and energy related requirements

## Slide 3: TDMA Receiver Block
Preprocessor

## Slide 4: Systems Level Power Analysis Flow
TDMA Rosetta Model
CMOS Power Model
Software Power Model
Define facet models for
Individual domains
CMOS TDMA
Software TDMA
Combine interacting facet models
to represent components
CMOS Power Model
Projection
Software Power Model
Projection
Project to analysis domain to
support predictive analysis
CHOOSE IMPLEMENTATION TECHNOLOGY
Trade-off analysis is possible early
in the systems design process
Interaction
Interaction
Interactions define impact of
design on energy consumption
Analyze
Analyze
Analysis using both simulation and
analytic techniques

## Slide 5: Defining the Interaction
Power
TDMA Function
Interaction
SW Power
CMOS Power
Extension
Inferred
Interactions
1. Define functional and basic power domain model
2. Define interaction between function and power
3. Define technology specific power models by specializing power domain
4. Infer interactions between function and new technology power models
5. Perform trade-off studies at the systems level for any technology specific
implementation that extends the basic power domain

## Slide 6: Power Domain Model
domain power is
p, nominal, leakage::posreal;
activity::posreal;
calculateOpActivity(opSet::sequence(label))::posreal;
export all;
begin state_based_semantics
p1: p' = activity + leakage;
end domain power;
Basic Model of Computation for power consumption
Based on activity and state change
Defines the power consumed by a state change
Does not specify the specifics of state change

## Slide 7: CMOS Power Model
facet cmos_power(leak::design posreal) is
usage_plus::posreal ; usage_minus::posreal;
usage_not::posreal; usage_equal::posreal;
usage_and::posreal;
calculateOpActivity(opSet::sequence(label)):: posreal is
if (opSet == nil) then 0
else case head(opSet) is
"+" -> 0.2 * usage_plus | "-" -> 0.015 * usage_minus |
"not" -> 0.01 * usage_not | "=" -> 0.3 * usage_equal |
"=>" -> 0.04 * usage_equal |
"and" -> 0.015 * usage_and
end case + calculateOpActivity(tl(opSet))
end if;
export all;
begin power
c1: leakage = leak;
end facet cmos_power;
Extends power domain to specialize for CMOS
MoC remains state-based

## Slide 8: Software Power Model
facet sw_power(Vcc,leak::design posreal) is
calculateOpActivity(opSet::sequence(label)):: posreal is
if (opSet == nil) then 0
else case head(opSet) is
"+" -> 0.4 * Vcc | "-" -> 0.35 * Vcc |
"not" -> 0.27 * Vcc | "=" -> 0.1 * Vcc|
"=>" -> 0.7 * Vcc | "and" -> 0.3 * Vcc
end case + calculateOpActivity(tl(opSet))
end if;
export all;
begin power
s1: leakage = leak;
end facet sw_power;
Extends power domain to specialize for software
MoC remains state-based

## Slide 9: Power / Function Interaction Model
interaction DandP(f::discrete; g::power) is
begin logic
discrete_to_power: reflect.meta_equal
(g.activity,
g.calculateOpActivity(reflect.meta_getOperators(f)));
power_to_discrete: {};
end interaction DandP;
Models interaction between a discrete state semantics and energy use
Projects new terms into the power model based on function performed
Energy use calculated in terms of operator activity
Energy use does not affect functional correctness

## Slide 10: TDMA Receiver Block Modeled
Component modeled for demo
Preprocessor

## Slide 11: What the demo does…
SW Resampler
Power Model
Power Model
Resampler Model
SW Specific
Power Model
CMOS Specific
Power Model
CMOS Resampler
Power Model
1. Start with power and Resampler requirements
2. Write CMOS power model
3. Derive CMOS Resampler power model using interaction
4. Write software power model
5. Derive software Resampler power model using interaction
Power models are derived by
understanding the interaction
between technology and function
Evaluate
Model
Evaluate
Model

## Slide 12: Derived Software Power Model
Terms generated to reflect software specific power calculation
facet sw_power(Vcc :: design posreal is 3.3; leak :: design posreal) is
calculateOpActivity(opSet :: sequence(label)) :: posreal is
if (opSet == nil) then 0
else case head(opSet) is + -> 0.4 * Vcc | - -> 0.35 * Vcc | not -> 0.27 * Vcc |
= -> 0.1 * Vcc | => -> 0.7 * Vcc | and -> 0.3 * Vcc
end case + calculateOpActivity(tl(opSet))
end if;
export ALL;
begin power
s1: leakage = leak;
discrete_projection:
activity = calculateOpActivity(=, =>, %, =, ', =>,=, -, and, =, ', =, ');
p1: p' = activity + leakage;
end facet sw_power

## Slide 13: System Models
bitvector12::subtype(bitvector) is sel(x::bitvector | #x = 12);
getMaxResampleRate(rate::integer)::integer is
case rate is
4 -> 6 | 8 -> 6 | 7 -> 8 | 12 -> 5 | 13 -> 3 | other -> 10
end case;
increment_count(count,maximum::integer)::integer is
if (count >= maximum) then 0 else count+1
end if;
facet resampler(I,Q::in bitvector12;clk::in bit;modRate:: design integer;
Iresampled,Qresampled::out bitvector12) is
count,maximum::integer;
begin discrete
getMax:maximum=getMaxResampleRate(modRate);
getcount:(%clk) => (count' = increment_count(count,maximum));
resample:(count = maximum - 1)=> (Iresampled'=I) and (Qresampled' =Q);
end facet resampler

## Slide 14: Power / System Interactions
facet cmos_resampler(I,Q:: in bitvector12;clk::in bit;
modRate:: in integer;
Iresampled,Qresampled::out bitvector12;
leak::design posreal) is
begin logic
t1: DandP(resampler(I, Q, clk, modRate, Iresampled, Qresampled),
cmos_power(leak));
end facet cmos_resampler;
facet sw_resampler(I,Q:: in bitvector12;clk::in bit;
modRate:: in integer;
Iresampled,Qresampled::out bitvector12;
Vcc,leak::design posreal) is
begin logic
t1: DandP(resampler(I, Q, clk, modRate, Iresampled, Qresampled),
sw_power(Vcc, leak));
end facet sw_resampler;

## Slide 15: Domain Organization
logic
continuous
discrete
discrete-time
finite-state
continuous-time
frequency
RF
digital
sequential-machine
state-based
signal-based
Unit of
Semantics
Model of
Computation
Engineering
Modeling
CSP
trace-based
synchronous

## Slide 16: Domain Interactions
logic
continuous
discrete
discrete-time
finite-state
continuous-time
frequency
RF
digital
sequential-machine
state-based
signal-based
Extensions
CSP
trace-based
synchronous
Homomorphisms
Partial Morphisms

## Slide 17: Tracking Systems-Level Issues
logic
continuous
discrete
discrete-time
finite-state
continuous-time
frequency
RF
digital
sequential-machine
state-based
power
continuous-power
cont-time-power
frequency-power
RF-power

## Slide 18: Rosetta and Systems Level Design
Addressing heterogeneity is critical to systems level design
  Domain specific modeling
  Multiple functional views
  Constraints and requirements
Language level solutions can help address heterogeneity issues
  Interactions between modeling domains
  Projections and morphisms between models
Rosetta provides semantics and tools for integrating heterogeneous systems specifications
  Initial studies and examples demonstrate effectiveness

## Slide 19: More Information
Rosetta language information
  Documentation and Tools at http://www.sldl.org
  Issue tracking at http://bugzilla.ittc.ku.edu
Rosetta standardization
  Biweekly teleconferences
  http://www.eda.org/slds-rosetta/
  Contact Dr. Perry Alexander alex@eda.org
Rosetta events
  Tutorials at FDL’02 and HDLCon’03 (tent.)
  DAC BoF Session
  1st Annual Rosetta Workshop following DAC