Closed-Loop and

Open-Loop Gain

Consider the inverting amplifier—a feedback amplifier constructed with an op-amp:

The open-circuit voltage gain of this amplifier:

is also referred to by engineers the closed loop gain of the feedback amplifier.

Q:  Closed loop? What does that mean?

A:  The term “closed loop” refers to loop formed by the feed-forward path and the feed-back (i.e., feedback) path of the amplifier.

In this case, the feed-forward path is formed by the op-amp, while the feed-back path is formed by the feedback resistor R2.

If the loop is broken, then we say the loop is “open”.  The gain () for the open loop case is referred to as the open-loop gain.

For example, in the circuit above we know that:

Combining, we find the open-loop gain of this amplifier to be:

Of course, once we “close” the loop, we have an amplifier with a closed-loop gain of:

which of course is the open-circuit voltage gain of this inverting amplifier.

Note that the closed-loop gain () does not explicitly involve the op-amp gain Aop.

*	The closed-loop gain is determined by two resistor values, which typically are selected to provide significant gain (), albeit not so large that the amplifier is easily saturated.

*	Conversely, the open-loop gain (-Aop) obviously does involve the op-amp gain.  Moreover, as in this case, the open-loop gain of a feedback amplifier often only involves the op-amp gain!

*	As a result, the op-amp gain is often alternatively referred to as the open-loop gain.

Note that closing the feedback loop turns a generally useless amplifier (the gain is too high!)  into a very useful one (the gain is just right)!

# Text boxes

Open-Loop

Closed-Loop

v+

v-

R1

R2

ideal

vin

-

+

Feed-forward

Path

Feed-back

Path

v+

v-

R1

R2

ideal

vin

-

+

i1

i2

v+

v-

R1

R2

ideal

vin

-

+