The Virtual Short

For feedback amplifiers constructed with op-amps, we have found (and will continue to find) that the two op-amp terminals will always be approximately equal ().

Of course, this must be true in order to avoid saturation, as the gain of an op-amp is ideally infinitely large.

Since  for feedback applications, it appears that the two op-amp terminals are shorted together!

There is no short inside the op-amp!

The condition in op-amp feedback amplifiers where  is known as the “virtual short”.

Remember, although the two input terminal appear to be shorted together, they are most certainly not!

If a true short were present, then current could flow from one terminal to the other (i.e., ).  However, we know that the input resistance of an op-amp is ideally infinite, and thus we know that the input current  into an op-amp is zero.

Therefore, it is not the op-amp that enforces the condition , it is the feedback that makes this so!

The virtual short: your new BFF

Applying the concept of a virtual short can greatly simplify the analysis of an op-amp feedback amplifier.

For example, consider again the inverting amplifier:

The virtual ground

This time, we begin the analysis by applying the virtual short condition:

Since the non-inverting terminal is grounded (v+ = 0), the virtual short means that the non-inverting terminal is likewise at zero potential (v- = 0)!

We refer to this condition as a virtual ground.

Isn’t this simpler?

Analyzing the remainder of the circuit, we find:

Combining, we find:

Rearranging, we again find the open-circuit, closed-loop voltage gain:

Your TA is even smarter than this guy!

# Text boxes

i2

i1

R1

R2

ideal

vin

-

+

Note this is exactly the result we found before, yet in this case we never considered the op-amp equation:

The virtual short equation () replaced the op-amp equation in our analysis of this feedback amplifier.

Eeffectively, the two equations say the same thing (provided Aop is infinitely large, and we have negative feedback in the circuit).

i2

i1

R1

R2

ideal

vin

-

+

ideal

v+

i1

vin

R1

v-

i2

-

+

R2

open

circuit

vo

-

+

v+

v-

“Virtual Short”

v+

v-

vo

-

+