The Weighted Summer

Consider an inverting amplifier with multiple inputs!

From KCL, we can conclude that the currents are related as:

and because of virtual ground (), we can conclude from Ohm’s Law:

The output voltage

Likewise:

Inserting these results into the initial KCL expression:

Now, we sprinkle on some algebraic pixie dust,  and find the output voltage:

The output is thus a weighted summation of each of the input signals!

We therefore refer to this circuit as the weighted summer.

How to combine signals

Note that if , the output is an unweighted summer:

For example, if:

then:

The summer is a method for combining several signals!

# Text boxes

i

R3

R2

i3

i2

i1

v2

v1

R1

Rf

ideal

vout

v3

-

+

i

R3

R2

i3

i2

i1

v2

v1

R1

Rf

ideal

vout

v3

-

+