Special Problem 2.4-2

## For the circuit  above, determine:

## 1.  output vout in terms of inputs v1 and v2.

## 2.  both the differential and common-mode gains of  this amplifier.

3.  the  CMRR.

# Text boxes

R3

=2K

R1 =4K

R2 =2K

v2

v1

vout

ideal

-

+

R4 = 1K

R5 =9K