Superposition and

Op-Amp Circuits

Consider this op-amp circuit, with two input voltages (v1 and v2):

The easiest way to analyze this circuit is to apply superposition!  Recall that op-amp circuits are linear, so superposition applies.

Our first step is to set all sources to zero, except v2 —in other words, set v1 =0 (connect it to ground potential):

Since the current into the non-inverting input of the op-amp is zero (), it is evident that:

Likewise, the remainder of the circuit is simply the non-inverting amplifier, where:

Combining these two equations, we get:

Now for the second step.  Turn off all sources except v1 —in other words set v2 =0:

It is evident that the since the current into the non-inverting terminal of the op-amp is zero, the voltage v+ is likewise zero.

Thus, the circuit above is simply an inverting amplifier, where:

There are no more sources in this circuit, so that we can conclude from superposition that the output voltage is the sum of our two, single-source solutions:

Note this circuit is effectively a weighted difference amplifier.

# Text boxes

v2

R3

R4

R4

R3

v2

v1

ideal

vout

-

+

R1

R2

ideal

vo2

-

+

R1

R2

R4

R3

v1

ideal

-

+

R1

R2

vo1