Special Problem  –  5.5-8

The capacitors in this circuit are very large.

Determine the small-signal voltage gain of this amplifier.

Determine the small-signal input resistance of this amplifier.

# Text boxes

K= 1 mA/V2

Vt= 1.0 V

= 0.01 V-1

2.5 K

10 K

10 K

vi

4.5 V

10 K

4 K

10 V

+

vo

-

ii