Example: Small-Signal BJT Approximations

Say that we wish to find the collector current  of a BJT biased in the active mode, with   and a  base-emitter voltage of:

Q:  Easy!  Since:

we find:

right?

A: Although  this answer is definitely correct, it is not very useful to us as engineers.  Clearly, the base-emitter voltage consists of a D.C. bias term (0.6 V) and a small-signal term ().

Accordingly, we are interested in the D.C. collector current  and the small-signal collector current .  The D.C. collector current is obviously:

But how do we determine the small-signal collector current  from:

???

The answer, of course, is to use the small-signal approximation.

We know that:

where:

Therefore, the small-signal collector current is approximately:

and therefore the total collector current is:

Q: Say the D.C. bias voltage increases from  to .  What happens to the BJT collector current?

A:  The  D.C. bias current becomes:

since the transconductance is now:

the small-signal collector current is:

Quite an increase!

Changing the transistor operating point (i.e., the DC bias point) will typically make a big difference in the small-signal result!