Amplifier Transfer Function

Note that the ideal amplifier transfer function:

is an equation of a line (with slope = Avo and y -intercept = 0).

This ideal transfer function implies that the output voltage can be very large, provided that the gain Avo and the input voltage vin  are large.

However, we find in a “real” amplifier that there are limits on how large the output voltage can become.  The transfer function of an amplifier is more accurately expressed as:

This expression is shown graphically as:

- This expression  (and graph) shows that electronic amplifiers have a maximum and minimum output voltage (L+ and L-).

- If the input voltage is either too large or too small (too negative), then the amplifier output voltage will be equal to either L+ or L- .

- If vout = L+ or vout =L- ,  we say the amplifier is in saturation (or compression).

Amplifier saturation occurs when the input voltage is greater than:

or when the input voltage is less than:

Often, we find that these voltage limits are symmetric, i.e.:

For example, the output limits of an amplifier might be L+ = 15 V and L- = -15 V.

However, we find that these limits are also often  asymmetric (e.g., L+ = +15 V and L- = +5 V).

For example, consider a case where the input to an amplifier is a triangle wave:

Since  for all time t, the output signal will be within the limits L+ and L- for all time t, and thus the amplifier output will be vout (t) = Avo vin (t):

Consider now the case where the input signal is much larger, such that  for some time t (e.g., the input triangle wave exceeds the voltage limits  and  some of the time):

Note that this output signal is not a triangle wave!

For time t where , the value  is greater than L+ and less than L-, respectively.  Thus, the output voltage is limited to  for these times.

As a result, we find that output  does not equal  —the output signal is distorted!

In reality, the saturation voltages  are not so precisely defined.  The transition from the linear amplifier region to the saturation region is gradual, and cannot be unambiguously defined at a precise point.

# Text boxes

vout

vin

Avo > 0

Avo

vin

vout

Q:  Why do we care if an amplifier saturates? Does it cause any problems, or otherwise result in  performance degradation??

A:  Absolutely!  If an amplifier saturates—even momentarily—the unavoidable result will be a distorted output signal.

vin (t)

t

t

vout (t)

t

vin (t)

This is precisely the situation about which I earlier expressed caution.  We now must experience the palpable agony of signal distortion!

t

vout (t)

Avo

vin

vout

L+

L-

L+

L-

t

vout(t)

Avo < 0