Small-Signal Analysis of

Multi-Stage Amps

Consider a multi-stage amplifier like the earlier example:

Q:  How do we analyze such a big circuit?

A:  Well, the DC analysis is simplified (for this case), since each stage is connected with a DC blocking (AC coupling) capacitor.  Since capacitors are open circuits at DC, the circuit above turns into 3 separate DC circuits with 3 separate DC solutions:

Q:  Great. That works for DC analysis, but for small-signal analysis the large capacitors become approximate shorts, and the three stages become inextricably connected.  Do we just have to analyze one great big small-signal circuit?

A:  Certainly we could replace each transistor with its small-signal equivalent circuit, and then analyze the entire resulting mess to find the overall open-circuit voltage gain, input resistance, and output resistance.  However, there is an alternate way!

Recall what we learned in Chapter 1.  We can fully characterize an amplifier with its open-circuit voltage gain, its input resistance, and its output resistance.  We these parameters, we can replace even the most complex amplifier with a simple equivalent model:

We can likewise do this for each stage of a multi-stage amplifier!  We can:

- “Disconnect” a single stage from the stages preceding it and the stages after it.

- Then apply a small-signal analysis to just that stage, and find the small-signal open-circuit voltage gain, the input resistance, and the output resistance of just that single stage.

- Then form a simple, equivalent amplifier circuit for that stage, and use this small-signal equivalent circuit in the overall multi-stage circuit.

What we are left with looks like a problem from Chapter 1—a string of cascaded amplifiers where we know nothing more than the 3 fundamental parameters of each:

# Text boxes

+

vi

-

Ro

Ri

+

-

BJT Diff Pair

Output

Stage

Gain

Stage

Input

Stage

-

+

Common-Emitter

Common-

Collector