Special Problem 6.6-1

# For the differential amplifier shown below, the DC components of vI1 and vI2 are equal.

Both transistors Q1 and Q2 are in saturation.

The transistors are identical, with K= 1mA/V2 and Vt = 1.0 V

Find the small signal differential gain Ad = vo1/vd  for the differential amplifier shown below.

# Text boxes

15 V

vI1

10 K

20 K

10 K

10 K

- 15 V

15 V

vI2

10 K

10 K

10 K

vo1

vo2

Q1

Q2

2 mA