## Slide 1: Virtual Companion Robot for Senior Citizens
Kyle Berkley
Matthew MacKay
Martin Nganga
Juzer Zarif

## Slide 2: Motivations and Use Case
Considerable population of senior citizens reside in old age home like facilities
High chance of loneliness in these settings (1)(2)
Traditional pets require “maintenance” (3)
Empathetic virtual companion serves as possible alternative
Could provide additional services as well
References:
http://thenationshealth.aphapublications.org/content/48/8/E39
https://www.tandfonline.com/doi/full/10.1080/01634372.2018.1478352
https://www.aspca.org/pet-care/dog-care/general-dog-care

## Slide 3: Initial Design
Attempted to use Raspberry Pi for person detection using haar cascade.
Pi’s processing couldn’t produce an acceptable frame rate with haar cascade analysis (5 to 10 fps)
Needed something with more processing power/something with hardware acceleration
Possible solutions included higher power x86 machine (expensive).
A couple of forum users suggested the JeVois machine vision module

## Slide 4: JeVois Machine Vision Module
Video sensor + Quad core CPU + USB video output + Serial output
Used provided ArUco marker library for reliable and fast detection (output frame rate 15 - 25 frames per second)
JeVois sends module output as serial messages containing information about the location of the marker
Easy to interface with an Arduino Mega over serial
Utilize serial messages from JeVois to control pan-tilt motion using servo motors connected to Arduino Mega.
Zero in on pan angles by actuating motors.

## Slide 5: Obstacle Avoidance
Initially design called for three ultrasonic sensors
Initial algorithm only checked for objects in front and looked for best way around
Problems:
  Not enough sensors to cover front of robot
  Ultrasonic sensors provide inconsistent and unreliable data (i.e. shiny, dark, or non-flat surfaces)
Final design uses seven IR sensors in front of robot that provide a “shield”
Final algorithm works like a protective “shield”. If any object pierces the “shield”, the robot will either turn out of the way or stop if there is no way out
IR sensors overall deal with less data, are more accurate, and have less latency than ultrasonic sensors

## Slide 6: Software
React Native for mobile application development allowing cross-platform development (create iOS and Android apps simultaneously)
Use Expo CLI to enable the use of a simulator for the iOS and Android development process
Dynamically generate new Aruco Markers and accept medication information on the mobile app.
Display

## Slide 7: Future expandability
Use native capabilities to communicate send communication over Bluetooth to Raspberry Pi
Train the machine vision module to identify and approximate the location of a specific user instead of an ArUco marker
Better autonomous collision avoidance (more powerful processor?)
Robot could track health data and provide assistance when needed
Expand the target demographic for the virtual companion robot by adding smarter empathy response (virtual babysitter)
Implement a GUI for the robot or a face to make it more of a companion.
https://youtu.be/eFX_fh0F8-0

## Slide 8
QUESTIONS?